# Copyright 2015

# Metal Roof Innovations, Ltd.

www.S-5.com

# SECTION 07 72 55

# ROOF ACCESSORY UTILITY ATTACHMENT SYSTEM

This section has been prepared by Metal Roof Innovations, Ltd. for use in the preparation of a project specification. Attachment may be by one of the following methods:

S-5! Clamps: A non-penetrating system for use on standing seam metal roofs.

The following should be noted in using this specification:

Notes are included to assist the user in editing the section to suit project requirements. These notes are included as hidden text, and can be revealed or hidden by one of the following methods:

Microsoft Word: From the pull-down menus select TOOLS, then OPTIONS. Under the tab labeled VIEW, select or deselect the HIDDEN TEXT option.

Corel WordPerfect: From the pull-down menus select VIEW, then select or deselect the HIDDEN TEXT option.

Hypertext links to specific websites are included after manufacturer names and names of organizations whose standards are referenced within the text, to assist in product selection and further research. Hypertext links are contained in parenthesis, e.g.:

(www.S-5.com)

Optional text requiring a selection by the user is enclosed within brackets, e.g.: "Section [09 00 00.] [_____.]"

Items requiring user input are enclosed within brackets, e.g.: "Section [_____ - ________]."

Optional paragraphs are separated by an "OR" statement, e.g.:

**** OR ****

"Green" requirements are included for projects requiring LEED certification, and are included as green text. For additional information on LEED, visit the U.S. Green Building Council website at www.usgbc.org.

For assistance on the use of the products in this section, contact Metal Roof Innovations, Ltd. by calling 888-825-3432,, by email at info@S-5solutions.com, or visit our website at www.S-5.com.

- - GENERAL

1.1 	SUMMARY

Edit the following paragraphs to include only those items specified in this section.

    - Section Includes:

      - Utility Attachment for metal roofs.

      - Non-penetrating attachment system.

  - RELATED SECTIONS

Coordinate the following paragraphs with other sections in the project manual.

A. 	Division 01: Administrative, procedural, and temporary work requirements apply to this section.

B. 	Section 07 41 13 - Metal Roof Panels

C. 	Section 07 61 00 - Sheet Metal Roofing

D. 	Section 07 62 00 – Sheet Metal Flashing and Trim

- Section 07 72 53 – Snow Guards

- Section 13 34 19 – Metal Building Systems

- Section 27 05 29 – Hangars and Supports for Communication Systems

  - REFERENCES

    - Aluminum Association (AA) (www.aluminum.org) - Aluminum Standards and Data, 2003 Edition.

    - ASTM International (ASTM) (www.astm.org):

      - B85-03 - Standard Specification for Aluminum-Alloy Die Castings.

      - B221-04a - Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Profiles, and Tubes.

  - SUBMITTALS

Limiting submittals to only those actually required helps to minimize liability arising from the review of submittals. Minimize submittals on smaller, less complex products.

Include the following for submission of shop drawings, product data, and samples for the Architect's review.

    - Action Submittal:

      - Shop Drawings: Include roof plans showing locations of utility attachment on roof and attachment details and spacing.

      - Product Data:

        - Product description.

        - Construction details.

        - Material descriptions.

        - Individual component dimensions.

        - Finishes.

        - Installation instructions.

      - Samples:

        - Clamp samples.

        - 12-inch long attachment member samples including all associated hardware.

    - Informational Submittals:

      - Test results: Results of product tensile load testing of attachment clamp, issued by a recognized independent testing laboratory, showing ultimate load-to-failure value of attachment.

Include the following for submission of closeout submittals for the Owner’s record purposes.

    - Closeout Submittals:

      - Certification: Installer's certification that utility attachment system was installed in accordance with manufacturer's instructions and approved Shop Drawings.

  - QUALITY ASSURANCE

    - Manufacturer Qualifications: Manufacturer to specialize in production of Metal Roof Attachment Products of the type specified with a minimum of 20 years documented experience.

    - Installer Qualifications: Installer to specialize in metal roof installation and installation of Metal Roof Attachment Products with a minimum of 5 years documented experience.

Include the following for full size mockups for review of construction and coordination of work of several sections.

    - Mockup:

      - Size: Minimum [8] [__] feet long.

      - Show: Utility attachment clamps, utility attachment members, and accessories.

      - Locate [where directed.] [____.]

      - Approved mockup may remain as part of the Work.

  - DELIVERY, STORGE AND HANDLING

    - Deliver components to jobsite properly packaged to provide protection during transport, delivery and handling.

    - Store products in manufacturer’s original labeled and unopened packaging in a clean and dry location, protected from potential damage, until ready for application.

- - PRODUCTS

  - SYSTEM DESCRIPTION

Include the following for utility system installed using S-5! clamps on standing seam roofs only.

    - Attachment system to provide attachment to standing seam metal roofs:

      - With only minor dimpling of panel seams.

      - Without penetrations through roof seams or panels.

      - Without use of sealers or adhesives.

      - Without voiding roof warranty.

B.       Performance Requirements: Provide utility attachments to withstand exposure to the weather and environmental elements, and resist design forces without failure due to defective manufacture.

  - MANUFACTURER

    - Acceptable Manufacturer: S-5! Metal Roof Innovations, Ltd., 8655 Table Butte Road, Colorado Springs, CO.  80908; Tel: 888-825-3432; Fax: 719-495-0045; Email: support@s-5.com; Web: www.s-5.com (www.S-5.com)

Edit the following to indicate whether or not substitutions will be permitted for the products in this section.

    - Substitutions: Not permitted.

2.3 	UTILITY ATTACHMENT SYSTEMS FOR STANDING SEAM METAL ROOFS

Include the following for roofs using S-5! non-penetrating attachment clamps.

A.	Basis of Design: S-5! Utility System manufactured by S-5! Metal Roof Innovations, Ltd.

B. 	Components:

      - Clamps

a. 	Manufactured from 6061-T6 aluminum extrusions conforming to ASTM B221 or aluminum castings conforming to ASTM B85 and to AA Aluminum Standards and Data.

1) 	Model: S-5! Standard Mini Clamp No. [S-5-U MINI.] [S-5-S MINI.] [S-5-T MINI.] [S-5-Z MINI.] [S-5-E MINI.] [S-5-Q MINI.] [S-5-H MINI.] [S-5-K700 MINI.] [S-5-H90 MINI.] [S-5-N MINI.] [S-5-N 1.5 MINI.] [S-5-KHD MINI.] [S-5-V MINI.] [S-5-K Grip MINI.] [S-5-R465 MINI.]

2) 	Model: S-5! Flanged Mini Clamp [S-5-USF MINI.] [S-5-EF MINI.] [S-5-ZF MINI]

b. 		Set screws: 300 Series stainless steel, 18-8 alloy, 3/8 inch diameter, with round head point.

c. 		Attachment bolts: 300 Series stainless steel, 18-8 alloy, 8 mm diameter, hex flange bolt.

Include the following when using S-5! Standard Mini Clamp attachment to standing seam roofs.

2. Flange Adapter:

        - Manufactured from 6061-T6 or 6005-T5 alloy and temper aluminum extrusions conforming to ASTM B221 and AA Aluminum Standards and Data or cast aluminum.

          - Model: No. S-5-FA

3. Utility Attachment Cross Members:

        - Manufactured from 6061-T6 or 6005-T5 alloy and temper aluminum extrusions conforming to ASTM B221 and AA Aluminum Standards and Data.

        - Track in top and bottom to receive 8 mm diameter, hex flange nut.

          - Model: Dual Grip Strut

PART 3- EXECUTION

  - EXAMINATION

A. Prior to beginning installation, verify that:

1. 	Panel seaming is complete.

2.   	Panel attachment is sufficient to withstand loads applied by utility attachment system.

3.	Installation will not impede roof drainage.

  - PREPARATION

          - Clean areas to receive attachments; remove loose and foreign matter that could interfere with installation or performance.

3.3	INSTALLATION

- Install system in accordance with manufacturer's instructions and approved Shop Drawings

Include the following for roofs using S-5! Standard Mini Clamp attachment.

B. 	S-5! Utility System:

      - Place clamps at maximum 32 inches on center or as required by in-service loads.

      - Place clamps in straight, aligned rows.

      - Tighten set screws to manufacturer's recommended torque. Randomly test set screw torque using calibrated torque wrench.

      - Attach flange adapter to clamp; tighten bolts to manufacturer’s recommended torque.

      - Attach utility attachment cross members to flange adapter; tighten bolts to manufacturer's recommended torque.

      - Do not cantilever utility attachment cross members more than 4 inches beyond last clamp at ends.

*****OR****

Include the following for roofs using S-5! Flanged Mini Clamp attachment.

B. 	S-5! Utility System:

- Place clamps at maximum 32 inches on center or as required by in-service loads.

- Place clamps in straight, aligned rows.

- Tighten set screws to manufacturer's recommended torque. Randomly test set screw torque using calibrated torque wrench.

- Attach utility attachment cross members to clamps; tighten bolts to manufacturer's recommended torque.

- Do not cantilever utility attachment cross members more than 4 inches beyond last clamp at ends.

# END OF SECTION